## Slide 1
NEW JERSEY TURNPIKE AUTHORITY Bringing Resilience into Business as Usual
New Jersey Coastal Flooding Technical Workshop
Prepared by Dewberry for the New Jersey Turnpike Authority and public presentation. March 19, 2025

## Slide 2: Agenda
Resilience Program Overview
Exposure and Vulnerability
Standard Operating Procedures
Next Steps

## Slide 3: What is Resilience?
Resilience is the ability to:
1
BEFORE EVENT Prepare for and Adapt to changing conditions
2
DURING EVENT
Withstand
3
AFTER EVENT
Respond to and recover rapidly from disruptions
Notes: Resilience can mean different things in different contexts and it is important to ask the questions – Resilience to Whom, What, When, Where and Why because it informs the answers. For our purposes we are using the FHWA definition.
The definition: “anticipate, prepare for and adapt to changing conditions and withstand, respond to and recover rapidly from disruptions.”
We are doing this for our people and our patrons, looking at longer term trends such as sea level rise and sudden storms and impacts on the Turnpike and Garden State Parkway. Specifically, we are focused on addressing the impacts of flood hazards such as sea level rise, storm surge, inland fluvial (riverine) and pluvial (stormwater) flooding, and temperature increases. In the future, we may look at additional hazards as well.

## Slide 5: Turning Knowledge into Action
Activities
Inputs
Outputs
Outcomes
Impact
A Safe, Efficient, Innovative, and Resilient Toll Road System
A system that promotes continuous mobility, adapts to future climate conditions, operates sustainably, and maintains long term financial viability.
Enhanced planning
Targeted investments
Climate Informed Design
Sustainable operations and construction practices
Data, Models, Assessments
Policies and Plans
Partnerships
Resilient infrastructure
Enhanced traffic efficiency
Innovative technologies
Sustainable practices
Reduced risk
Cost savings
Prolonged asset life

## Slide 6: Roadmap to Resilience
IDENTIFY Resilience Solutions
DEFINE
Climate-Related Hazards
ASSESS
Risk and Vulnerability
ADVANCE & INTEGRATE
Resilient Infrastructure
Innovate
Analyze threats to assets, system-level service, and customer mobility.
Understand asset-level and system-level exposure and vulnerabilities.
Consider strategies across operations including procurement, capital planning, asset management, and state of good repair.
Design and construct resilient infrastructure projects to maximize return on investment over a project’s useful life considering future conditions.
Communicate
Educate
Activities:
Flood exposure assessment
Flood Exposure Visualization Tool
Activities:
Vulnerability pilots
Risk metrics
Activities:
Resilience Plan
Resilient Design Criteria and SOPs
Activities:
Resilience policy statement
Communications plan
Building Regional partnerships
Notes: Note: animation has been applied here so each click will define the roadmap strategy and a second click will reveal related activities.
The Resilience Program and Roadmap provides a coordinated structure to build on and grow the Authority’s existing resilience and sustainability activities. To support program growth into the future and meet the Authority’s strategic goals -- we developed a vision for a resilient Authority and the roadmap to get us there.
The roadmap will help us advance and integrate resilient infrastructure solutions across our plans, policies, procedures, designs and projects. And it is intended to help integrate resilience thinking into our core work by identifying climate change related threats, understanding asset- and system-level exposure and identifying resilience solutions.
The roadmap and this approach are supported by communication (internal and external awareness raising), education (training and technical assistance), and innovation (monitoring and evaluating progress and incorporating learning as we go to continue to improve and innovate).
Today’s focus is on the second step, ASSESS. We’ll also be briefly reviewing the first step, DEFINE, to share the results that informed our vulnerability assessment.

## Slide 7: Building Resilience through Risk Informed Decision Making
Long-term System Planning
Sustainable, Resilient Systems
Risk-Informed
Decision Making
Condition of Asset
Vulnerability of Asset
Criticality of Asset
Prioritized Projects
1
Screen Existing Capital Projects for Flood Risk and Resilience Needs
2
Identify and Prioritize Potential Resilience Projects
3
Standardize Approach for Considering Resilience in Construction
Notes: Condition of Asset: Current state of our transportation assets including maintenance needs.
Vulnerability: The degree to which an asset/system is susceptible to, or unable to cope with adverse effects of climate change or extreme weather events.
Criticality: Importance of the asset to the system/region/state/nation as a whole with respect to level of service and operation
By understanding the asset's condition, vulnerability, and criticality, we can make better-informed choices on how to allocate resources and where to invest to suppo long-term planning and climate resilience. By embracing a comprehensive, risk-informed approach, we can make sure that our toll-road system remains safe, efficient, and in a state of good repair for generations to come.

## Slide 8
EXPOSURE ASSESSMENT
Define Climate-Related Hazards

## Slide 9
Overview
Flood sources
  Riverine
  Coastal
  Stormwater
Time period
  Current
  2050
  2070
  2100
Frequency
  10 year
  100 year
Emissions Scenario
  RCP 4.5
x
x
x
8 exposure scenarios
=
Notes: First, we performed a model-based flood exposure assessment. The first step was to scope the most important flood scenarios and time horizons to model.
It was important to model all the major flood sources including riverine flooding, coastal flooding, and stormwater or pluvial flooding. Riverine and stormwater in 1 framework with coastal assessed separately
We also looked at four time periods that span the lifetime of Authority assets: the current period, 2050, 2070, and 2100.
We looked at relatively frequent 10-year event and relatively rare 100-year events.
Finally, we looked at a relatively high-emissions RCP 8.5 scenarios. This is a relatively conservative scenarios that assumes a continuation of recent historic trends in global greenhouse gas emissions.
We therefore looked at a total of total of eight scenarios.

## Slide 10: Exposure Methodology Highlights
Model: HEC-RAS v6.0 (plus coastal analysis)
Mesh resolution: ~10m (variable)
DEM: NJ 10ft LiDAR
Land cover: 2015 NJDEP Dataset
Infiltration: SCS CN Approach
Rainfall:
  Current: Atlas-14
  Future: NJ Extreme Precipitation Projection Tool
Discharge:
  Current: FEMA studies, Streamstats
  Future: HEC-HMS
Coastal elevations:
  Current: FIS
  Future: 2021 NJ Sea Level Rise Guidance
Major limitations:
  No explicit modeling of subsurface drainage system (e.g., stormwater inlets, pipes, outfalls)
  No fine resolution flood control structures (e.g,.floodwalls)
Assessment is more likely to overestimate flooding than underestimate flooding.
Notes: mention HEC-RAS, that this is a custom hydro model, and mention limitations.
This slides summarizes some of the technical details of the exposure assessment.
We’ll review them very briefly, but we’d be happy to find time to discuss these in more detail with anyone who is interested.
We used the HEC-RAS model to simulate flooding, along with some specialized coastal analysis.
The average model mesh resolution was approximately 30m with higher resolution along the highway and river corridors.
We used 10ft DEM and 2015 Land Use Land Cover data, both provided by New Jersey state agencies.
We used the SCS curve method to simulate variable infiltration across different land use and soil types.
We obtained design storm rainfall data for current conditions from NOAA Atlas-14, and for future conditions from the NJ Extreme Precipitation Tool.
We obtained larger stream and river discharge data for current conditions from the FEMA flood insurance studies and Streamstats. For Future conditions, we used a set of representative HEC-HMS hydrology models to develop future change factors.
We obtained coastal elevations for current conditions from the FEMA flood insurance studies and for future conditions from the 2021 NJ Sea Level Rise Guidance.
In order to do flood modeling at this scale, it was not possible to explicitly model the subsurface drainage system, such as stormwater inlets, pipes, and outfalls). These are represented in a very course way by the infiltration approach.
We also could not explicitly model the fine resolution flood control structures, like flood walls.
As a results of these limitations and the study design in general, the assessment is more likely to overestimate flooding that underestimate flooding.
It was important for the exposure analysis to capture all the potential flood exposure, so that more detailed checks could be done if there if there is actual flood exposure.

## Slide 11: Case Study – Data into Action

## Slide 12: Risk Metrics

## Slide 13
VULNERABILITY ASSESSMENT
Assess Risk and Vulnerability

## Slide 14: Overview
Flood Exposure
Whether the asset is located in an area experiencing direct effects of flooding
Adaptive Capacity
The ability of the transportation network to recover quickly following a shock or stress to the asset
Sensitivity
How the asset performs during and after a flood exposure event
Vulnerability Methodology
Notes: Scott
Our vulnerability methodology follows an approach consistent with FHWA.
How
Exposure
Likelihood of exceeding flood exposure metrics – depth, duration, velocity, force
Sensitivity
Asset-specific design and condition evaluations
Adaptive Capacity
High-level, qualitative assessment

## Slide 15: Five Pilot Sites
Irvington
Mt Laurel
Westerly Alignment
Heards Brook
Cheesequake

## Slide 16: Improved Flood Modeling
Model IMPROVEMENT | Exposure Assessment | Vulnerability Pilots
Hydraulic structures | Openings added in terrain to allow flow through at significant cross-drainage structures | Physical structures added using as-built data if available or approximation method based on imagery and terrain
Rainfall scenarios | Rainfall simulation for 10- and 1-percent AEP Existing condition, 2050 condition, and 2100 condition | Rainfall simulation for events ranging from 50-pecent to 0.2-percent AEP. Rainfall depth ranges between upper and lower 90-percentile Existing condition, 2050 condition, and 2100 condition
Terrain | 10m USGS DEM | 1m USGS DEM
Boundary conditions | Fluvial inflows using regression equation method from USGS StreamStats website Pluvial simulated as rainfall-on-grids 10-percent AEP coastal surge elevation | Fluvial/pluvial simulated as rainfall-on-grids MHHW coastal surge elevation
Model extent | Half-mile buffer from roadway | Five areas of interest (AOI), and relevant intersecting watersheds
Model resolution | 200 feet x 200 feet | 100 feet x 100 feet

## Slide 17: Asset-Specific (Irvington Site GSP MP 143.6) Flood Depth Probability Tables – Ex. 1
 | Recurrence Interval (years) |  |  |  |  |  |  |  | 
Flood Depth (ft) | 2020 | 2030 | 2040 | 2050 | 2060 | 2070 | 2080 | 2090 | 2100
0.5 | 10 | 8 | 7 | 6 | 6 | 6 | 6 | 6 | 6
1.0 | 13 | 11 | 9 | 8 | 8 | 8 | 8 | 8 | 7
1.5 | 25 | 19 | 15 | 12 | 12 | 12 | 12 | 12 | 11
2.0 | 51 | 35 | 26 | 20 | 20 | 20 | 19 | 19 | 18
2.5 | 278 | 152 | 95 | 66 | 64 | 63 | 61 | 60 | 58
3.0 | >500 | >500 | 303 | 185 | 182 | 175 | 169 | 167 | 161
3.5 | >500 | >500 | >500 | >500 | >500 | >500 | 500 | 476 | 476
4.0 | >500 | >500 | >500 | >500 | >500 | >500 | >500 | >500 | >500
 | AEP - Annual Exceedance Probability (years) |  |  |  |  |  |  |  | 
Flood Depth (ft) | 2020 | 2030 | 2040 | 2050 | 2060 | 2070 | 2080 | 2090 | 2100
0.5 | 10% | 12% | 14% | 15% | 16% | 16% | 16% | 16% | 17%
1 | 8% | 9% | 11% | 12% | 13% | 13% | 13% | 13% | 13%
1.5 | 4% | 5% | 7% | 8% | 8% | 8% | 9% | 9% | 9%
2 | 2% | 3% | 4% | 5% | 5% | 5% | 5% | 5% | 5%
2.5 | 0% | 1% | 1% | 2% | 2% | 2% | 2% | 2% | 2%
3 | <0.2% | <0.2% | 1% | 1% | 1% | 1% | 1% | 1% | 1%
3.5 | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | 1% | 1% | 1%
4 | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | <0.2% | <0.2%
Notes: Example
Irvington Site
GSP MP 143.6
NBI 361436t
Major Culvert

## Slide 18: Wave Effects
With future conditions,
  Increases to base flood elevation (surge + waves)
  Increases in potential damage from larger waves

## Slide 19: Wave Data Development
Source data: USACE North Atlantic Coast Comprehensive Study, 2015
  Wave heights provided at nodes for:
    Current conditions
    1 meter (3.3. feet) sea level rise
Wave Heights (feet), Current Conditions: 0 feet SLR |  |  |  |  |  |  | 
Node | e10 | e20 | e50 | e100 | e200 | e500 | e1000
91147 | 2.26 | 2.45 | 2.69 | 2.85 | 2.98 | 3.11 | 3.18
91148 | 2.27 | 2.45 | 2.68 | 2.85 | 2.97 | 3.10 | 3.18
91160 | 2.27 | 2.46 | 2.69 | 2.84 | 2.98 | 3.11 | 3.18
91794 | 2.27 | 2.45 | 2.69 | 2.85 | 2.98 | 3.10 | 3.18
Wave Heights (feet), Future Conditions: 3.3 feet SLR |  |  |  |  |  |  | 
Node | e10 | e20 | e50 | e100 | e200 | e500 | e1000
91147 | 2.46 | 2.70 | 2.96 | 3.12 | 3.26 | 3.41 | 3.51
91148 | 2.85 | 3.23 | 3.64 | 3.89 | 4.10 | 4.34 | 4.49
91160 | 2.54 | 2.81 | 3.11 | 3.29 | 3.44 | 3.61 | 3.72
91794 | 2.25 | 2.42 | 2.61 | 2.72 | 2.82 | 2.93 | 3.01
Nodes extracted near NJTA assets
  Significant wave heights converted to controlling wave heights
  Scenarios for 1 and 2 feet of SLR were linearly interpolated
  Wave height increases capped in areas of limited fetch

## Slide 20: Wave Assessment: Cheesequake Creek

## Slide 21: Vulnerability Scoring
Source: U.S. DOT Gulf Coast Study, Phase 2 Fact Sheet (FHWA-HEP-14-053))
Customized application of USDOT Vulnerability Assessment Scoring Tool (VAST) Framework
Three components:
  Exposure
  Sensitivity
  Adaptive Capacity

## Slide 22: Scoring Indicators – Roadways
Exposure
Flood Depth ExCo 10yr
Sensitivity
Hazard 2 ExCo AEP
Adaptive Capacity
Roadway Type
Hazard 2 ExCo AEP Increase by 2050
Flood Depth ExCo 100yr
Flood Depth 10yr Increase by 2050
Flood Depth 100yr Increase by 2050
Coastal Flood Depth ExCo 10yr
Coastal Flood Depth ExCo 100yr
Coastal Flood Depth 10yr Increase by 2050
Coastal Flood Depth 100yr Increase by 2050
How much will the asset be exposed?
Will flood exposure cause asset failure?
How quickly can the system adapt to asset impairment?

## Slide 23: Vulnerability Scoring Results (Pilots)
VULNERABILITY COMPONENTS | SCORE | ROAD SEGMENTS | WATERWAY BRIDGES | OVERLAND BRIDGES | CULVERTS | BUILDINGS | ALL ASSETS
Exposure | 1 | 141 | 14 | 116 | 8 | 65 | 344
 | 2 | 149 | 5 | 1 | 8 | 28 | 191
 | 3 | 14 | 0 | 1 | 2 | 4 | 21
 | 4 | 1 | 6 | 0 | 0 | 0 | 7
 | 5 | 0 | 0 | 0 | 0 | 0 | 0
Sensitivity | 1 | 101 | 1 | 118 | 0 | 55 | 275
 | 2 | 35 | 15 | 0 | 15 | 9 | 74
 | 3 | 95 | 9 | 0 | 3 | 15 | 122
 | 4 | 73 | 0 | 0 | 0 | 18 | 91
 | 5 | 1 | 0 | 0 | 0 | 0 | 1
Adaptive Capacity | 1 | 30 | 1 | 7 | 3 | 1 | 42
 | 2 | 45 | 6 | 68 | 9 | 51 | 179
 | 3 | 54 | 7 | 19 | 2 | 40 | 122
 | 4 | 60 | 11 | 24 | 3 | 2 | 100
 | 5 | 116 | 0 | 0 | 1 | 3 | 120
Total Vulnerability Score | 1 | 12 | 2 | 39 | 1 | 28 | 82
 | 2 | 141 | 12 | 79 | 12 | 47 | 291
 | 3 | 133 | 9 | 0 | 5 | 20 | 167
 | 4 | 19 | 2 | 0 | 0 | 2 | 23
 | 5 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 24
SOPs
Identify Resilient Solutions

## Slide 25: SOP Workflow
Identify Asset
Screen for Hazards and Impacts
Identify Applicable Component SOP(s)
Perform Qualitative Risk Considerations
Determine Appropriate Resilience Interventions

## Slide 26: Questions?
Mat Mampara, P.E.
Vice President
MMampara@Dewberry.com
Sara Margolis, ENV SP
Project Manager
SMargolis@Dewberry.com
Notes: Thank you