## Slide 1
2026 New Jersey Coastal and Climate Resilience Conference
March 9, 2026| 12:00 PM
Where Planning Meets Action:
Strategies for Smarter Coastal Resilience
Wendy Laurent, P.E., WEDG

## Slide 2: Purpose and Presentation Outline
OUTLINE
Fort Pierce Beach– permit flexibility supports rapid action
Volusia County Beaches– countywide planning + foundational community support
Martin County SPP– template modifications for SLR adaptation
Healthy, well-maintained beaches are essential to resilient coastal communities
  Benefits of beaches:
    Reduce storm-related forces, minimizing damage to landward infrastructure
    Dynamic features that allow for recovery following storms
    Naturally adapt to the impacts of SLR
    Also support recreation, enhance ecological value, and contribute to local economies
Lessons Learned from three case studies
  Demonstrate how proactive planning and strategic decision-making can strengthen beach management practices
2
1
3

## Slide 3: Fort Pierce Beach
PERMIT FLEXIBILITY SUPPORTS RAPID ACTION

## Slide 4: Fort Pierce Project Background
Location– Fort Pierce Beach, St. Lucie County, FL
Erosion hot spot has led to numerous studies and changes to the federal project
  First constructed in 1971, 5-year nourishment interval
  2006 Limited Reevaluation Report  2-year nourishment interval
  2026? General Reevaluation Report/Section 203 Study  erosion control structures
Project Area, ~1.4 miles
Monitoring Area, ~1 mile

## Slide 5: Fort Pierce Project Background
Project Area, ~1.4 miles
Monitoring Area, ~1 mile
since initial construction
7,600,000 cy
Federal dredging events
6,700,000 cy
Year | Nourishment Type
2018 | Dredge (Federal)
2020 | Truck Haul (County)
2021 | Dredge (Federal)
2023 | Dredge (Federal)
2025 | Truck Haul (County)
2026 | Dredge (Federal)
= ~240,000 cy per year
NOURISHMENT STATS
Supplemental County events
900,000 cy
= ~140,000 cy per year

## Slide 6: 2023 Federal Nourishment
March – May 2023
Placed ~490,000 cy across ~1.4 miles
Fort Pierce Beach Pre-Construction Condition 2023
Fort Pierce Beach Post-Construction Condition 2023
Fort Pierce Beach During Construction 2023

## Slide 7: 2025 Federal Nourishment
Planned 2025 USACE nourishment
Fort Pierce Beach February 2025 Conditions
  First solicitation (October 2024)– no bids received
  Second solicitation (January 2025)– bids 2x government estimate
Project postponed 1 year
Erosion too close for comfort going into hurricane season

## Slide 8: 2025 Emergency Truck Haul
Pivot from dredging project to emergency truck haul project before the summer season
  Contractor mobilized within 1 month after postponed project
  March – April 2025; placement of ~95,000 cy in the erosion hot spot
Fort Pierce Beach Pre-Construction Condition 2025
Fort Pierce Beach Post-Construction Condition 2025
Fort Pierce Beach Construction 2025

## Slide 9: 2026 Federal Nourishment
USACE held Industry Day– Consolidate projects? Bid all separately?
Fort Pierce Beach Closure Due to Erosion
Fort Pierce Beach January 2026 Condition
Fort Pierce Beach January 2026 Condition
  Bids received! Anticipated mobilization late March 2026 (not soon enough…); planned placement of ~400,000 cy across ~ 1 mile
Notes: No hurricanes in 2025 but beach still eroded significantly due to nor’easters

## Slide 10: Lessons Learned & Proactive Project Management
BUILD FLEXIBILITY INTO PERMITS
PLAN AHEAD
EMERGENCY SAND PLACEMENT CONTRACTS

## Slide 11: Lessons Learned & Proactive Project Management
Sand sources
  Borrow area
  Upland sand mine
  Channel/AIWW/Fort Pierce Harbor
  Sand Trap
Placement methods
  Dredge
  Truck Haul
EMERGENCY SAND PLACEMENT CONTRACTS
BUILD FLEXIBILITY INTO PERMITS
PLAN AHEAD

## Slide 12: Lessons Learned & Proactive Project Management
BUILD FLEXIBILITY INTO PERMITS
Expedite contracting
Contractor ready to mobilize *almost* immediately
EMERGENCY SAND PLACEMENT CONTRACTS
PLAN AHEAD
Permits, environmental timelines
Industry availability
  Host industry days
    Projects in the same region
    Projects with similar means and methods
Contractor Mobilization One Month After Postponed Federal Project

## Slide 13: Volusia County Beaches
COUNTYWIDE PLANNING + FOUNDATIONAL COMMUNITY SUPPORT

## Slide 14: Volusia County Beaches
47 total miles of beach with 15 miles designated for beach driving and 27+ miles classified as critically eroded
Key destinations include Daytona Beach and New Smyrna Beach
Annual beach tourism generates $4.3 billion in regional economic impact
Severely impacted by Hurricanes Ian and Nicole (2022)
  Erosion of 6.4 Mcy (-34 cy/ft)
  Sand starved environment
Limited active beach management

## Slide 15: Volusia County Beaches
47 total miles of beach with 15 miles designated for beach driving and 27+ miles classified as critically eroded
Key destinations include Daytona Beach and New Smyrna Beach
Annual beach tourism generates $4.3 billion in regional economic impact
Severely impacted by Hurricanes Ian and Nicole (2022)
  Erosion of 6.4 Mcy (-34 cy/ft)
  Sand starved environment
Limited active beach management

## Slide 16: Path to Stability

## Slide 17: Path to Stability

## Slide 18: Path to Stability
WHO
WHAT
WHERE
WHEN
WHY
OUTREACH & ENGAGEMENT
ALTERNATIVES ANALYSIS
RISK ASSESSMENT

## Slide 19: WHERE Risk Assessment – Methodology
1
Shoreline Encroachment
the horizontal distance (or “buffer”) between the MHW shoreline position and infrastructure
2
Infrastructure exposure
or the “elevation buffer”; Percentage of parcels where infrastructure is within or below 1 ft of the USACE SACS 1% AEP SWEL
vulnerability parameters  community risk index
3
Historical Erosion Rate
the average shoreline change rate since 2016 calculated via linear regression
2
1
…
…
Other Factors
armoring presence and exposure; SBEACH storm response; community demographics; etc.

## Slide 20: Geospatial Analysis
Parcel-by-parcel community average
  Categorized and marked upland infrastructure for each parcel
    Non-essential, accessory components of a property not included
    Coastal armoring features
Calculated the elevation at each infrastructure/armoring point using LiDAR data
  Distance between significant feature- infrastructure, armoring, MHW
Structure to MHW: 150 ft
Structure Elevation: + 23 ft-NAVD88
MHW

## Slide 21: Risk Assessment – Results
Quantified risk utilizing a high/medium/low scoring system
  Bins based on results
  Each community received a score and rank
  Easily comprehended by the public
Included additional information for decision making
Allows for prioritization of projects across communities
POINTS
points
=
risk

## Slide 22: WHAT Shoreline Alternatives Analysis
  No Action
  Structural Relocation
  Flood Proofing and Structural Elevation
  Seawalls
  Revetments
  Beach Nourishment
  Groins
  Nearshore Sand Placement
  Breakwaters
  Nearshore Artificial Reefs
Investigate beach management alternatives and their applicability to the County’s shoreline reaches
Alternatives include
No ACTION
Beach Nourishment
BREAKWATERS

## Slide 23: Shoreline Alternatives Analysis – Methodology
Taylor Engineering | 23
1
DEFINE OBJECTIVES
2
does not meet objective
partially meets objective
fully meets objective
Reduce coastal storm damages to structures, critical infrastructure, and cultural resources
Reduce risk of natural resource loss
Reduce risk to life safety
Avoid impact to recreation
Minimize impacts to threatened and endangered species and their habitats
Comply with federal, state, and local policies and regulations
COMPILE BACKGROUND INFORMATION
function, benefits and drawbacks, risk and uncertainties, social considerations, large-scale feasibility, $$$
RANK OBJECTIVES
3
DOWN SELECT ALTERNATIVES  APPLY JUDGMENT  RECOMMENDATIONS

## Slide 24: Outreach and Engagement
Two series of meetings– 3 hours/evenings/locations
  Brief presentations to introduce topics followed by poster sessions
  Meeting 1 study kickoff- introduced the study and reviewed current beach conditions
  Meeting 2 results & preliminary recommendations- shared risk assessment findings; discussed shoreline management alternatives; presented top ranked alternatives
Two public surveys
  Beach usage and quality– over 12,000 responses!
  Future management of beaches

## Slide 25: Volusia’s Path Toward Stability
Feasibility Study
Current Management Actions
Risk
Community Feedback
Shoreline Alternatives
Analysis
Management Actions

## Slide 26: Martin County SPP
TEMPLATE MODIFICATIONS FOR SLR ADAPTATION

## Slide 27: Martin County Shore Protection Project (SPP)
Northern-most 4 miles of Martin County– Stuart & Jensen Beach
Consistent overtopping of the berm + increased nourishment
The County asked Taylor Engineering to investigate options to modify the project design to increase the performance of the beach fill and enhance resilience
    Summarize project history & available data
    Analyze historic beach trends
    Initiate discussions with project partners + permitting agencies
    Model current and alternative templates using XBEACH
    … recommendations and next steps

## Slide 28: Beach Nourishment History
2,229,780 cy
3,567,780 cy
GDM: Renourishment of 589,000 every 11 years (53,600 cy/yr)
LRR: Renourishment of 787,800 cy every 13 years (60,600 cy/yr)
Some quick math of what has been occurring…

## Slide 29: Project Design Parameters
4 construction templates
Variable reference datums
  Tidal vs geodetic datums
    MHW; MSL; MLW
    NAVD88; NGVD29
MHW varies over project design life
  Construction template elevations consistent

## Slide 30: Water Level History and Projections
Observed

## Slide 31: Water Level History and Projections
Observed
Martin County SPP’s 1993 General Design Memorandum:

## Slide 32: Alternatives Analysis
authorized design dependent on tidal datum  increase in SLR (high)  increase in volume?
Coordination with USACE
Analysis of four alternate construction templates (XBEACH modeling)
  Design limitations
  Analyze performance through contour tracking; volume changes; profile wetting
  Iterative process to optimize design
  Back berm

## Slide 33: Successes and Lessons Learned
Planned renourishment (March 2026) is implementing the new modified template!
How do we make changes to a project over the project lifetime due to SLR or increased erosion rates? Authorizing documents lay the foundation
Beach resilience directly related to “buffer” volume and recovery time/conditions
  Increased volume and strategic sand placement led to increased performance
Project partner relationships are critical for success

## Slide 34
THANK YOU
QUESTIONS?
Wendy Laurent, P.E., WEDG
Associate Vice President, Coastal Engineer, Philadelphia Office Lead
wlaurent@taylorengineering.com
TOGETHER, THESE CASE STUDIES UNDERSCORE THE IMPORTANCE OF PROACTIVE PLANNING, ADAPTIVE PERMITTING, AND COMMUNITY ENGAGEMENT FOR RESOURCE MANAGERS AND DECISION-MAKERS WORKING TO PROTECT INFRASTRUCTURE, ENHANCE COASTAL RESILIENCE, AND ENSURE LONG-TERM COMMUNITY SUSTAINABILITY