## Slide 1
Jon Compton, AJ Riggs, Anushka Samant, Ellen Neises, Ellen Kohler, Brianne Callahan, John Henderson, Ahmad Payab, Nirajan Adhikari, and Franco Montalto*
Development of the 2025 Camden Coastal Resilience Plan

## Slide 2: Overview of presentation
Project origin and process
The focus on flood mitigation
Five resilience strategies
Four early investments

## Slide 3: Project Origin and Team
Project lead:
  The Center for Environmental Transformation (CFET)
Funding:
  National Fish and Wildlife Foundation (NFWF) Community Capacity Building and Planning Grant (Phase 1)
Project Team:
  PennPraxis, eDesign Dynamics, the Penn Water Center, and Drexel University (through CCMUA)

## Slide 4: Strategic Alignment
NFWF goals
Community resilience
Nature-based solutions
Increase in (contiguous) habitat with connected corridors
NFWF positioning - prepare for future phases of the NFWF grant program:
Phase 2: Site assessment and preliminary design
Phase 3: Final design and permitting
Phase 4: Restoration implementation
Neighborhood, City, and State Priorities and Plans
There are and have been many!
CCMUA goals
85% reduction in CSOs to the Cooper River

## Slide 5: Our 18-month process
Stakeholder interviews
Formation of a Technical Advisory Panel (decision-makers and professionals in the space)
Formation of a Project Steering Committee (neighborhood orgs and community leaders)
Focus group meetings
One-on-one meetings with key stakeholder groups
Onboarding of community ambassadors
Community meetings and workshops
Site visits across Camden
Site visits to other cities

## Slide 6: Flooding – the top priority for residents, the City, and the county

## Slide 11: Leveraging CCMUA’s LTCP Process
Currently developing alternatives for its LTCP and is committed to reducing both CSOs into the Cooper and Delaware River and flooding

## Slide 12: Understanding flooding in a coastal CSO city
Regional modeling 🡪 2D HEC-RAS
Localized site investigations 🡪 Scalgo
Detailed H&H Modeling 🡪 1D-2D integrated all pipes PCSWMM model

## Slide 13: Key Findings

## Slide 22
10 PROJECTS THAT REDUCE FLOODING

## Slide 25: Simulated flooding resulting from January 2024 flood event

## Slide 26: Mitigated flooding, January 2024 flood event

## Slide 27
GATEWAY-FARNHAM PARK AREA
PHOTO CREDIT: JON COMPTON
COOPER RIVER
GATEWAY PARK
FARNHAM PARK
PENNSAUKEN
BAIRD BLVD
THE PUB
ADMIRAL
WILSON
BLVD
MARLTON
NEIGHBORHOOD

## Slide 28
CURRENT FLOODING PROBLEM IN EAST CAMDEN
COOPER RIVER
GATEWAY PARK
FARNHAM PARK
PENNSAUKEN
BAIRD BLVD
THE PUB
ADMIRAL
WILSON
BLVD
MARLTON
NEIGHBORHOOD

## Slide 29
COOPER RIVER
FLOODABLE
PARK AREA
ADMIRAL
WILSON
BLVD
MARLTON
NEIGHBORHOOD
TRAIL ON AN
ELEVATED BERM
FLOODABLE
PARK AREA
BERM
ELEVATING THE LINK TRAIL IN GATEWAY PARK WILL CREATE A BERM OR LEVEE THAT PROVIDES FLOOD PROTECTION BY PREVENTING THE COOPER RIVER FROM SWELLING INTO ADMIRAL WILSON BOULEVARD AND MARLTON’S RESIDENTIAL AREA.

## Slide 30
Projects align with neighborhood, city, and state priorities and plans
Cooper River Gateway West Vision Plan, 2014
Gateway Park Management Plan (New Jersey Conservation Foundation), 2018
My East Camden Neighborhood Plan, 2021
Lakes Management Plan, 2022
Current Camden County Municipal Utility Authority efforts to develop the Long-Term Control Plan
DEP site remediation plans
City and County redevelopment projects and priorities
Phase 1 Loop of LINK Trail to go into construction in 2027
Kayak Launch to go into construction in 2025
Gateway Park Management Plan: New Jersey Conservation Foundation. 2018.
Cooper River Gateway West Vision Plan. Philadelphia: Cairone & Kaupp, Inc., 2014.

## Slide 31: Next steps
WITH SUPPORT FROM THE WILLIAM PENN FOUNDATION, WE ARE ADVANCING THREE NEXT STEPS:
MODELING SEWER BACKUPS AND FLOODING TO REDUCE CSO BURDEN IN MARLTON
DEVELOPING DESIGN DRAWINGS FOR A GREEN STORMWATER INFRASTRUCTURE PROJECT IN EAST CAMDEN (PROJECT #2A, #2B)
DEVELOPING EAST CAMDEN RESILIENCE PLAN IN PARTNERSHIP WITH SJCS
$133 K
$474 K
$315 K

## Slide 32: Follow up
Franco Montalto
fam26@drexel.edu

## Slide 33: Extra slides

## Slide 34: Regional 2D HEC-RAS Model

## Slide 35: Regional 2D HEC-RAS Model
Observed and modeled flow from all tributaries added to the 2D mesh

## Slide 36: Validation against flooding photos provided by stakeholders

## Slide 37: Localized site investigations
Scalgo supports “flash flood” and “Sea level rise” visualizations on terrain

## Slide 38: Localized site investigations

## Slide 39: 1D-2D all pipes PCSWMM model

## Slide 40
GATEWAY PARK FLOOD PROTECTION BERM + LINK TRAIL + SHORELINE RESTORATION
Estimated cost: $13.3M
Shoreline Restoration: 4.8 acres
Total Flood Volume Reduction: TBD
Total CSO Reduction: 5,662,000 gal
$/Gal of Flood Volume Reduction: TBD
$/Gal of CSO Reduction: $2.35/gal
#1 GATEWAY PARK FLOOD PROTECTION BERM + LINK TRAIL + SHORELINE RESTORATION

## Slide 41
SPORTS COURTS AND FIELDS
(PROJECT #3)
Estimated Cost: $11.8M
Total Flood Volume Reduction: 1,782,000 gal
Total CSO Reduction: 0 gal
$/Gal of Flood Volume Reduction: $6.6/gal
$/Gal of CSO Reduction: N/A
GATHERING, EVENT, AND PLAY SPACES (PROJECT #2)
Estimated Cost: $14.5M
Total Flood Volume Reduction: 87,000 gal
Total CSO Reduction: 2,790,000 gal
$/Gal of Flood Volume Reduction: $167/gal
$/Gal of CSO Reduction: $5.2/gal
ENVIRONMENTAL CENTER
Estimated Cost: $10M
#2 GATHERING, EVENT, AND PLAY SPACES
#3 SPORTS COURTS AND FIELDS
#4 ENVIRONMENTAL CENTER

## Slide 42
FARNHAM PARK LIVING SHORELINE
Estimated Cost: $10.6 M
Shoreline Restoration: 3.6 acres
# 5 FARNHAM PARK LIVING SHORELINE

## Slide 43
FILTRATION WETLAND
Estimated Cost: $9.6M
Total Flood Volume Reduction: 1,780,000 gal
Total CSO Reduction: 1000 gal
$/Gal of Flood Volume Reduction: $5.37/gal
$/Gal of CSO Reduction: $9560/gal
INDUSTRIAL PARK
Estimated Cost: $12.6M
Total Flood Volume Reduction: 1,784,000 gal
Total CSO Reduction: 0
$/Gal of Flood Volume Reduction: $7.03/gal
$/Gal of CSO Reduction: N/A
GREEN BULKHEAD
Estimated Cost: ~~$10M
Total Flood Volume Reduction: 1,780,000 gal
Total CSO Reduction: 0
$/Gal of Flood Volume Reduction: $0.56/gal
$/Gal of CSO Reduction: N/A
#6 FILTRATION WETLAND
#7 INDUSTRIAL PARK
#8 GREEN BULKHEAD FOR INDUSTRIAL AREA FLOOD PROTECTION

## Slide 44
COMBINED SEWER TREATMENT WETLANDS
Estimated Cost: $12.2M
Total Flood Volume Reduction: 143,000 gal
Total CSO Reduction: 340,000 gal
$/Gal of Flood Volume Reduction: $84.9/gal
$/Gal of CSO Reduction: $35.7/gal
#9 COMBINED SEWER TREATMENT WETLANDS
$12.2m

## Slide 45
GREEN STORMWATER INFRASTRUCTURE
Estimated Cost: $17.5M
Total Flood Volume Reduction: 1,849,000 gal
Total CSO Reduction: 62,000 gal
$/Gal of Flood Volume Reduction: $9.5/gal
$/Gal of CSO Reduction: $282/gal
#10 GREEN STORMWATER INFRASTRUCTURE