## Slide 1
Mind the Gap! Universities Building a Local Knowledge Base for Resilience
Panel Speakers
Philip Orton, Stevens
Jon Miller, Stevens
Michel Boufadel, NJIT
Thomas Grothues, Rutgers
Owen Thomas, Montclair
Tom Herrington, Monmouth
Kim McKenna, Stockton

## Slide 2: New Jersey Coastal Consortium for Resilient Communities
Established by the State of New Jersey in 2021
A multi‐disciplinary, multi-university consortium to advance coastal community resilience in New Jersey through actionable research.
Focused on improved understanding of coastal systems to identify practical solutions and responses to climate change.
Utilizing Barnegat Bay as a living laboratory to research climate change impacts on coastal lagoon estuarine systems in urban and natural environments.
Community Resilience

## Slide 3: New Collaborations and Modeling Tools to Help Predict Bay Flooding and Other Processes
Philip Orton
porton@stevens.edu
Funding from the New Jersey Coastal Resilience Research Consortium

## Slide 4: Motivation
Chronic high-tide and rain flooding

## Slide 5: Hurricane Sandy Simulation using ROMS/COAWST
COAWST: Coupled Ocean, Atmosphere, Wave and Sediment Transport modeling framework (Warner et al. 2010) with the widely-used open-source ROMS-3D hydrodynamic model
Applications (USGS): Barnegat Bay circulation, flushing, Hurricane Sandy impacts, tidal wetlands and sediment transport (Defne et al. 2016, 2019; Donatelli et al. 2018)
wind
wind
Model and simulation of N. Ganju and Z. Defne (Defne et al. 2019)
Manasquan
Barnegat Inlet
Little Egg Inlet

## Slide 6: Simulation Results with Surge Barriers
wind
Stevens applications
  Upgrade model to latest version of COAWST
  Simulate Hurricane Sandy with and without USACE surge barrier proposal   
  Study sensitivity of storm surge to wind stress parameterization
  Apply for NSF funding to study wind stress and storm surge
Other potential applications
  Wind wave impacts

## Slide 7: Outcomes
New Collaborations and Modeling Tools to Help Predict Bay Flooding and Other Processes
New MARACOOS-funded research project – collaboration between Orton, Kerr, Herrington
  Research into the drivers of flooding in the bays (Nathaniel Nwogwu’s poster on Monday)
  (ongoing) Development of a new SCHISM compound flood model and forecast system for the bays
  (ongoing) Deployment of new observational capabilities for bay flooding and waves
Let’s collaborate on other Barnegat Bay topics where these models can be useful!

## Slide 8: Forecasting Dune Impacts Using Data Driven Models
Stevens CERG
Jon K. Miller

## Slide 9: Approach
Data driven modeling
Storm Intensity
Beach Morphology
Engineering Demand Parameter
Fragility Curve
Probability of damage for a given storm and beach state

## Slide 10: Quantifying Physical Parameters Tied to Resilience
Bathymetry and bedform constrain flow and drag
Flow and drag parametrize sediment movement, surge, wave height and direction
Bedform parametrizes erosion and accretion
Bedform is a proxy of habitat type and function

## Slide 11
Challenges | Solutions
Spatial extent | Areal orthophotography
Turbidity/surface artifacts | Sonar
Shallow water navigation | Surface Robots
Ground-truthing | Underwater photography
Classification | Machine learning

## Slide 12: Building expertise
In capacity in ASV application
In software support of ML
In fundamental understanding
In simulation/modeling

## Slide 13
Center of Natural Resources, http://cnr.njit.edu

## Slide 14
Postdocs (6) and students (14 PhD)
December 28 2025
http://cnr.njit.edu

## Slide 15: Coastal Wetland Salinization Monitoring
Hypothesis: Due to evaporation, the pore water salinity exceeds that of seawater

## Slide 16: Location of Rutgers and MERI sites

## Slide 17: Setup in MERI
CTD sensors installed at 20 cm, 40 cm and 60 cm.
All CTD sensors connected to Diver-Link to transmit data to online to Diver-Hub.

## Slide 18
Table 1: Data collected by the NJIT team based on two stations (see Figures 1, 2, and 3) |  | 
Data | Rutgers Jacque Cousteau Reserve. (39.593141, -74.346927) Start time/date: 1:15 pm / October 19, 2022 | Meadowland Environmental Research Institute. (40.750700, -74.091034) Start time/date: 2:02 pm / December 2, 2022
Porewater salinity | 15-min measurement interval | 5-min measurement interval
Porewater temperature | 15-min measurement interval | 5-min measurement interval
Porewater pressure (water level) | 15-min measurement interval | 5-min measurement interval
Air temperature | 15-min measurement interval | 5-min measurement interval
Air relative humidity | 15-min measurement interval | 5-min measurement interval
Wind speed | 15-min measurement interval | 5-min measurement interval
Wind direction | 15-min measurement interval | 5-min measurement interval
Barometric pressure | 15-min measurement interval | 5-min measurement interval

## Slide 19: MERI – Porewater Salinity
July 1, 2024 – September 31, 2025
Salinity ranged ~10–25 PSU indicating brackish conditions.
Salinity increased with depth (20, 40, 60 cm).
Higher summer salinity due to evaporation and reduced freshwater input.

## Slide 20: MERI – Porewater Temperature
Temperature ranged from about -1 to 26 °C.
Surface layer responded strongly to seasonal air temperature changes.
Deeper layer (60 cm) showed more stable and buffered conditions.

## Slide 21: MERI – Air Temperature and Precipitation
Air temperature and precipitation influence porewater salinity.
Summer: higher temperatures increase evaporation and salt concentration.
Winter–spring rainfall dilutes salinity levels.

## Slide 22: Setup in JCNERR-Rutgers
CTD sensors installed at 20 cm, 40 cm and 60 cm.

## Slide 23: JCNERR – Porewater Salinity
July 1, 2024 – July 31, 2025
Salinity ranged from 10 to >70 PSU showing strong variability.
Surface layer (20 cm) showed the largest fluctuations.
High peaks related to tidal flooding and evaporation.

## Slide 24: JCNERR – Porewater Temperature
Temperature followed seasonal trends similar to MERI (~ 0-26 °C).
Shallow sensor reacted fastest to air temperature changes.
Deeper layers remained more stable throughout the year.

## Slide 25: JCNERR – Air Temperature and Precipitation
Summer air temperature averaged about 23–24 °C.
Lower precipitation and higher evapotranspiration enhanced salinity.
Storm events caused temporary salinity spikes due to coastal flooding.

## Slide 26: Study Site 1: 706 Market Street
Flow rate
Chart: Time (min)
Chart: Time (min)

## Slide 27
Geology & Economics of Beach Nourishment
By Owen Thomas
Sea Isle City Beach Nourishment Project
Photo by Andrew Mills, NJ Advance Media and NJ.com
Beach Nourishment
Numerical Model
Regional Study
Impact of Nourishment Efforts on Efficiency
Bridging the Gap

## Slide 28
Kimberly McKenna
Interim Executive Director
Coastal Research Center (CRC), Stockton University
Evaluation of Alongshore and Inlet Sediment Transport
Long Beach Island & Little Egg Inlet
The role of sediment in New Jersey’s coastal communities & habitats
NJCRC-NJDEP Coastal & Climate Resilience Conference
Galloway, NJ March 9-11, 2026
Photo courtesy T. Kingston 11/29/2020
Photo courtesy T. Kingston April 24, 2025

## Slide 29
Little Egg Inlet
NJCCRC
2023 Little Egg Harbor/Holgate echosounder, Little Egg Inlet hydrographic pilot study, sediment transport white paper
Long Beach Township, Monmouth University UCI, New Jersey Bay Islands Initiative
2023-2025 wave, current, water quality, topo/bathy studies at High Bar Islands, West Marshelder Island, and Clam Cove (bay island restoration)
USCRP/NJSGC/Monmouth UCI/US Naval Academy
2024-2025 Little Egg Inlet drifter/ADCP waves & currents/suspended sediment/ hydro-morphological modeling/TAC, student, & stakeholder engagement
NJDOT-OMR/The Nature Conservancy/Monmouth UCI
2023-2025 NJ Atlantic Back Bays Regional Sediment Framework/Sediment Quantity & Dynamics
TNC/Partnership Delaware Estuary/Monmouth UCI/Stevens
2024-2026 wave, current, water quality, topo/bathy studies at 5 marshes (establish pipeline for marsh restoration)
NJDEP Div Science & Research/Rutgers CRSSA/Monmouth UCI
2023-2026 development of Marsh Futures sediment data layer
LEVERAGING FUNDS/CRC PARTNERSHIPS/PROJECTS
Barnegat Inlet

## Slide 30
Little Egg Inlet
Brigantine Inlet
Moored ADCP
Planned drifter release
Filling Knowledge Gaps
Surface current patterns
Sediment & currents through inlets
Quantify how much is reaching shorelines & habitats
To keep up with sea level and climatic changes.
OUR OCEAN AND BACK BAY COMMUNITIES AND HABITATS NEED SEDIMENT!