## Slide 1
2026 New Jersey Coastal and Climate Resilience Conference
March 11, 2026
Modeling of Sediment Motion in Marshes to Evaluate Shoaling and Beneficial Use Options
Christopher Bender, Ph.D., P.E., BC.CE
Co-author: Michael Kabiling

## Slide 2: Study Purpose and Presentation Outline
Review historical and present marsh features, shoaling, and dredging to understand local conditions
Develop a model capable of evaluating water levels, waves, and mixed sand/fines sediment transport pathways
Simulate potential alternatives to reduce shoaling and dredging requirements, including beneficial use of dredged material (BUDM) alternatives
Develop recommendations for future dredged material management strategies
OUTLINE
Project Location
Study Overview
Modeling Methods
Study Findings

## Slide 3: Project Location
Naval Submarine Base Kings Bay (NSBKB)
Located in Cumberland Sound, near the St Marys River, GA
Annual dredging volumes for the base and entrance channel exceed 1M cy/yr
Some dredged material placed in on-base dredged material management areas (DMMAs, aka a CDF)
Some material placed along the coastline or in offshore disposal area

## Slide 4: Project Location
Naval Submarine Base Kings Bay, evolving marsh conditions
January 2025
December 1985

## Slide 5: Study Overview
Develop a model to simulate local hydrodynamics, wave conditions, mixed sediment transport
Simulate suspended sediment and bed sediment transport
  particle tracing to evaluate shoaling patterns
Apply the model to evaluate
  potential alternatives to reduce shoaling
  include the impacts of sea level change
  marsh restoration

## Slide 6: Study Overview
Prior studies provided valuable information
3D MIKE3 hydrodynamic, wave, sand and mud transport model (2016 to 2018)
  Geo-Marine and AECOM Joint Venture (GMA)
  Study collected water level, current, and sediment concentration data
Delft3D model for hydrodynamic, wave, and sediment transport near structures (2021)
  Integral Consulting Inc. (ICI)
  Athena Technologies Inc. collected and analyzed 16 vibracore samples

## Slide 7: Modeling Methods
MIKE3 model for hydro, waves, sediment transport, particle tracking
Based on existing NSBKB model
3D hydro and mixed-bed model
  Sand and silt
  Captures bedload and suspended sediment
  Erosion and deposition (shoaling)
Area of Interest

## Slide 8: Modeling Methods
Concurrent study examined past, present and future marsh conditions
  Marstel-Day and EAEST
Comparison of 1929 T-Sheets and the 2016 NWI datasets
  areas of loss and gain (~1,000 acre loss)
SLAMM modeling examined marsh changes by decade (2030 to 2080)
Provided critical data for MIKE3 model
  Studies shared info and alternatives

## Slide 9: Modeling Methods
Apply data collected in the 2018 study
  Water level
  Current velocity
  Sediment flux
  Allow for calibration and verification near NSBKB
  Demonstrate model’s capability for simulations

## Slide 10: Modeling Methods
Calibration
3 weeks

## Slide 11: Modeling Methods
Verification
2.5 months

## Slide 12: Modeling Methods
Calibration
Velocity

## Slide 13: Modeling Methods
Calibration
Sediment Flux

## Slide 14: Modeling Methods
Particle Tracing
Shows origin and settling location
Allows for evaluation of shoaling patterns

## Slide 15: Modeling Methods
Apply model to evaluate various alternatives
  Beneficial use of dredged material (BUDM)
    Marsh restoration and 5-year uplifts
    Potential to restore marshes and sinuosity of channels and reduce shoaling
  Structures within NSBKB to cut-off flow through the base
    Full blockage of flow
  Use of DMMAs and ODMDS
    Current practice
Examine alternatives to 2080 with marsh changes due to sea level change by decade
Perform life cycle analysis and multi-criteria decision analysis (MCDA)

## Slide 16: Conclusions
Model developed for marsh area near NSBKB
  Hydro, waves, sediment transport, particle tracing
  Calibrated and verified
  Alternatives analysis include sea level change and marsh impacts from 2030 to 2080
Alternatives evaluation for BUDM projects, structural alternatives, and status quo (DMMA/ODMDS)
BUDM and structural solution shown to significantly reduce future shoaling and dredging vs status quo
Recommendation to further explore BUDM project with initial marsh restoration and then 5-year uplifts

## Slide 17
THANK YOU
QUESTIONS?